 LIBAKEDA Guile Interface Specification

Author: Stephen Meier

Date: 11-8-2007

# Introduction with usage suggestions

LIBAKEDA provides a mechanism for running scheme (guile) macros. An interface is provided to give the scheme macros the ability to create, manipulate and destroy LIBAKEDA elements.

LIBAKEDA divides its structures into two groups, graphic objects “OBJECTS” that are found within schematic files and other structures which exist within LIBAKEDA to facilitate the manipulation of the schematics and symbols into structures such as project top levels, pages and net lists.

An application which utilizes LIBAKEDA should

1. Register aplication specific scheme functions that it requires for its configuration file
2. Call the c function:
  libakeda_init (application_resource_file_name);
libakeda_init will initialize the library, initialize a standard set of scheme functions, create a globally available default toplevel structure and then execute the application resource file. The application_resource_file should check/display its revesion and immediately call a function to load the libakeda resoruce configuration macro:

(define akedadatarc (getenv "AKEDADATARC"))

(load (string-append akedadatarc "/system-akeda-rc"))

The environmental variable AKEDADATARC must have been set to the path containing the script configuration files.

The application resource file should then use its own functions for application specific configuration.

Either use the scheme interface or the c interface to create a PAGE structure and then attach it to the current top level project “project_current”

# Important Global Variables

## project_current

TOPLEVEL * project_current;

# LIBAKEDA Configuration Functions

## component-library

Add a directory to the list of component (symbol) directories

(component-library "${AKEDADATA}/sym/mr-aep")

## source-library

Specify where source entities exist.
The string after this keyword should be a valid directory name.
You should have read access to this directory and all the files inside
the directory.
The order of the source-library keywords determines the order they
are displayed, but they are searched *backwards*, ie last one in this list
is searched *first*.
All environment variables *MUST* be in the form ${variable_name}

(source-library ".")

## set-schematic-read-script

Set the default schematic read script

(set-schematic-read-script "akeda_sch_read.scm")

## set-schematic-write-script

Set the default schematic write script

(set-schematic-write-script "akeda_sch_write.scm")

## set-symbol-read-script

Set the default symbol read script

(set-symbol-read-script "akeda_sym_read.scm")

## set-symbol-write-script

Set the default symbol write script

(set-symbol-write-script "akeda_sym_read.scm")

# LIBGEDA Color Configuration Functions

The color functions are usually called as part of the initialization sequence.
Look for them in the gschem-darkbg or gschem-lightbg

In all of the color modes:
the first string is the actual color name
the second string is the outline color name
the third string is the postscript color name
and the final 3 integers are the RGB values for PNG image files

## attribute-color

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

attribute-color index color_name outline_color ps_color_string
    int_red int_green int_blue

Example:

(attribute-color 5 "yellow" "yellow3" "1 1 0" 255 255 0)
## background-color

sets default background color

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

background-color index color_name outline_color ps_color_string
        int_red int_green int_blue

Example:

(background-color 0 "black" "null" "null" -1 -1 -1)

## boundingbox-color

Set the default bounding box color. The bounding box color is displayed whenever you request that actions (move/copy/place) use a bounding box instead of the default outline.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

boundingbox-color index color_name outline_color ps_color_string
        int_red int_green int_blue

Example:

(boundingbox-color 12 "orange" "orange" "null" -1 -1 -1)
## bus-color

Set the color of any new buses (does not effect existing buses). To change existing buses use the override-bus-color

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

bus-color index color_name outline_color ps_color_string
     int_red int_green int_blue

Example:

(bus-color 10 "green" "green3" "0 1 0" 0 255 0)
## detached-attribute-color

Set the color of detached attributes. Detached attributes are just text items which were attributes at one time. Detached attributes are created in conjunction with the 'Detach Attribute' command.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

detached-attribute-color index color_name outline_color ps_color_string
        int_red int_green int_blue

Example:

(detached-attribute-color 8 "red" "red3" "1 0 0" 255 0 0)
## graphic-color

Set the default graphics color. All new Lines, Boxes, Circles, and Arcs are effected by this keyword. Existing graphic objects are not effected by this keyword.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

graphic-color index color_name outline_color ps_color_string
  int_red int_green int_blue

Example:

(graphic-color 3 "green" "green3" "0 1 0" 0 255 0)

## grid-color

Set the default grid color.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

grid-color index color_name outline_color ps_color_string
  int_red int_green int_blue

Example:

(grid-color 7 "grey" "null" "null" -1 -1 -1)
## logic-bubble-color

Set the color of logic bubbles / circles.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

logic-bubble-color index color_name outline_color ps_color_string
  int_red int_green int_blue

Example:

(logic-bubble-color 6 "cyan" "cyan3" "0 1 1" 0 255 255)

## net-color

Set the color of any new nets (does not effect existing nets). To change existing nets use the override-net-color

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

net-color index color_name outline_color ps_color_string
     int_red int_green int_blue

Example:

(net-color 4 "blue" "blue3" "0 0 1" 0 0 255)
## net-endpoint-color

 Set the default net endpoint color.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

net-endpoint-color index color_name outline_color ps_color_string
 int_red int_green int_blue

Example:

(net-endpoint-color 2 "red" "red3" "1 0 0" 255 0 0)

## pin-color

Set the color of any new pins (does not effect existing pins).
To change existing pins use the override-pin-color

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

pin-color index color_name outline_color ps_color_string
        int_red int_green int_blue

Example:

(pin-color 1 "white" "grey" "1 1 1" 255 255 255)

## select-color

Set the default selection color. This include the bounding box in window selects and when objects are selected.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

select-color index color_name outline_color ps_color_string
        int_red int_green int_blue

Example:

(select-color 11 "orange" "orange" "null" -1 -1 -1)
## text-color

Set the color of any new text (does not effect attributes, see below). Existing graphic objects are not effected by this keyword.

Input parameters:

index	string represents an integer location within color table
color_name	string represents color name
outline_color	string represents outline color name
ps_color_string	string represents post script color name
int_red	string 0 - 255 for red value
int_green	string 0 - 255 for green value
int_blue	string 0 - 255 for blue value

text-color index color_name outline_color ps_color_string
      int_red int_green int_blue

Example:

(text-color 9 "green" "green3" "0 1 0" 0 255 0)

# LIBAKEDA SMOBS

Smobs (small objects) are used to make new data types available to scheme (guile). libakeda creates a few smobs to enable scheme scripts to manipulate the data structures functions.

## page_smob

page_smob contains a pointer to a PAGE structure.
## object_smob

object_smob contains a pointer to an OBJECT structure.
## attrib_smob

attrib_smob contains a pointer to an attribute.
# ARC Object Structure Functions

## ak-arc-new

For an existing OBJECT_SMOB create, initialize and attach an ARC structure

Input parameters:

object_smob	OBJECT_SMOB previously created for this arc
center_x	string represents the center x location
center_y	string represents the center y location
radius	string represents the radius
start_angle	string represents the start angle
end_angle	string represents the end angle
color	string represents the color number
line_style	string represents the line style
width	string represents the arc width

Example:

(ak-arc-new object_smob center_x center_y radius start_angle
 end_angle color line_style width)

# ATTRIB Structure Functions

## ak-attrib-get-name-value

## ak-attrib-set-value

## ak-attrib-get-angle

# BOX Object Structure Functions

## ak-box-new

For an existing OBJECT_SMOB create, initialize and attach a BOX structure

Input parameters:

object_smob	OBJECT_SMOB previously created for this box
top_left_x	string represents the top left x location
top_left_y	string represents the top left y location
bottom_right_x	string represents the bottom right x location
bottom_right_y	string represents the bottom right y location
color	string represents the color number
line_style	string represents line style
width	string represents line width

Example:

(ak-box-new object_smob top_left_x top_left_y
bottom_right_x bottom_right_y
color line_style width)

# BUSRIPPER Object Structure Functions

# CIRCLE Object Structure Functions

## ak-circle-new

For an existing OBJECT_SMOB create, initialize and attach a CIRCLE structure

Input parameters:

object_smob	OBJECT_SMOB previously created for this box
center_x	string represents the center x location
center_y	string represents the center y location
radius	string represents the radius
color	string represents the color number
line_style	string represents outline style
width	string represents outline width

Example:

(ak-circle-new object_smob center_x center_y radius
   color line_style width)

# COLOR Structure Functions

# COMPLEX Object Structure Functions

## ak-complex-new

Create, Initialize a COMPLEX object and attach it to the object_smob. The object_smob references an object that already has been created and attached to a PAGE

Input parameters:

page_smob	PAGE_SMOB previously created
x	string represents the x location
y	string represents the y location
angle	string integer rotational angle
mirror	string boolean horizontally mirror the object
embedded	string boolean is the object embedded in the file
basename	string file name of the complex object

Example:

(ak-complex-new object_smob x y angle mirror embedded basename)

## ak-complex-attach-object

Attach an object to a complex object.

Input parameters

complex_smob	OBJECT_SMOB
obj_smob	OBJECT_SMOB

Example:

(ak-complex-attach-object complex_smob obj_smob)

; ; complex_smob must have been previously created
; ; obj_smob must have been previously created

## ak-complex-add-new-pin

Add a pin to a complex object that is on the top level's current page. The specific complex object is found by its' refdes attribute

## ak-complex-eco-correction

Replace the footprint attribute of a complex component

# LINE Object Structure Functions

## ak-line-new

For an existing OBJECT_SMOB create, initialize and attach a LINE structure

Input parameters:

object_smob	OBJECT_SMOB previously created for this line
color	string represents the color number
line_style	string represents line style
start_x	string represents the start x location
start_y	string represents the start y location
end_x	string represents the end x location
end_y	string represents the end y location
width	string represents line width

Example:

(ak-line-new object_smob color line_style start_x start_y
end_x end_y width)
# NET Structure Functions

## ak-net-new

Add a new net to the active top level's current page and make the net the page's active net.

Usage:

(ak-net-new net_name_string)

## ak-net-net_eco_correction

Replace an old pin with a new one by

1) find the net that has the old pin
2) remove the old pin from the net
3) find the component on the flat page that matches the new_uref
4) find the pin for the found component
5) add the new pin to the net

# OBJECT Functions

## ak-object-get-attributes

## ak-object-new

Create a new OBJECT_SMOB

Input parameters:

obj_type	boolean defined in o_types.h
selected	boolean true if selected
visible	boolean true if visible
locked	boolean true if locked

Example:

(define my_obj_smob “”)
(define obj_type “N”)
(define selected #f)
(define visible #t)
(define locked #f)

(set! my_obj_smob (ak-object-new obj_type selected visible locked))

## ak-object-attrib-new

For an existing OBJECT_SMOB and an existing TEXT OBJECT_SMOB give the TEXT OBJECT_SMOB to the OBJECT_SMOB to have it converted to an attribute attached to the OBJECT_SMOB's object. The attrib type parameter tells the object_smod which list to attach the attribute to.

Input parameters:

object_smob	OBJECT_SMOB previously created, any type
text_obj_smob	TEXT OBJECT_SMOB previously created
attrib_type	string: “0” for symbol “1” for schematic

Example:

(define attrib_type “0”) ;; make the new attrib a symbol attrib

(ak-object-attrib-new object_smob text_obj_smob attrib_type)

# PAGE Structure Functions

## ak-page-attach-object

Attach an object to a page.

Input parameters

page_smob	PAGE_SMOB
obj_smob	OBJECT_SMOB

Example:

(ak-page-attach-object page_smob obj_smob)

; ; page_smob must have been previously created
; ; obj_smob must have been previously created

## ak-page-display

Have the top level's current page display itself.

Input parameters:

page_smob	PAGE_SMOB

Example:

(ak-page-display page_smob);

; page_smob was previously created

## ak-page-get-filename

Get the file name for the page smob

Example:

(ak-page-get-filename page_smob);

; page_smob was previously created

# PLACEHOLDER Object Functions

# PICTURE Object Functions

# PIN Object Functions

## ak-pin-new

For an existing OBJECT_SMOB create, initialize and attach a LINE structure

Input parameters:

object_smob	OBJECT_SMOB previously created for this pin
start_x	string represents the start x location
start_y	string represents the start y location
end_x	string represents the end x location
end_y	string represents the end y location
pin_type	string represents pin type (net or bus)
parent_obj_smob	OBJECT_SMOB previously created, complex or	busripper types

Example:

(ak-pin-new object_smob start_x start_y end_x end_y pin_type
 parent_obj_smob)

# SEGMENT Object Functions

## ak-segment-new

Create, Initialize a SEGMENT object and attach it to the object_smob. The object_smob references an object that already has been created and attached to a PAGE

Input parameters:

page_smob	PAGE_SMOB previously created
x1	string represents the start x location
y1	string represents the start y location
x2	string represents the end x location
y2	string represents the end y location
segment_type	string “0” for a net “1” for a bus

Example:

(ak-segment-new object_smob x1 y1 x2 y2 segment_type)

# SLOT Functions

# SLOT_ENTRY Functions

# TEXT Object Functions

## ak-text-new

Create and initialize a TEXT object and attach it to the object_smob. The object_smob references an object that already has been created and attached to a PAGE

Input parameters:

object_smob	OBJECT_SMOB previously created for new text
x	string represents the page location
y	string represents the page location
size	string represents the text size
alignment	string represents the text alignment
angle	string represents rotational angle
number_lines	string represents number of text lines
visible	string represents if text should normally be displayed
show_type	string represents how to display an attribute
color	string represents the color number

Example:

(ak-text-new object_smob x y size alignment angle number_lines visible
 show_type color)

## ak-text-set-string

Set the string of a TEXT object smob

Input parameters:

object_smob	OBJECT_SMOB previously created
new_string	character string

Example:

(define new_string “hello, world!”)

(ak-text-set-string object_smob new_string)

# TOPLEVEL Structure Functions

## ak-toplevel-new-page

Have the toplevel create a new page, add it to its page list and then return a PAGE_SMOB.

Input Parameters:

string filename

bool top_of_hierarchy

Example:

define filename “my_schematic.sch”;

define top_of_hierarchy true;

set! new_page_smob (ak-toplevel-new-page filename top_of_hierarchy);

## ak-toplevel-merge-page

# VERSION Object Functions